SAFETY DATA SHEET

## SECTION 1. PRODUCT AND COMPANY IDENTIFICATION

MANUFACTURER: TRANSENE COMPANY, INC.

# ADDRESS: DANVERS INDUSTRIAL PARK

# 10 ELECTRONICS AVENUE DANVERS, MA 01923,

# TEL: (978) 777-7860 FAX: (978)-739-5640

# WWW.TRANSENE.COM

#### EMERGENCY NO. 1-800-424-9300 CHEMTREC

| MATERIAL NAME: Ruthenium Etchant RU44 REVISED: April 2016 CHEMICAL FAMILY: Nitric acid/ceric ammonium nitrate aqueous solution Product Number: 060-RU44 |
| --- |
| SECTION 2. HEALTH HAZARD INFORMATION Hazard Statements H290 Corrosive to Metals: Category 1 H302 Acute toxicity Oral : Category 4 H312 Acute Toxicity Dermal: Category 4 H332 Acute toxicity Inhalation : Category 4 H314 Skin corrosion / Skin irritation : Category 1C H318 Serious eye damage / Eye irritation : Category 1 H371 Special target organ systemic toxicity single exposure: Category 2 H373 Special target organ systemic toxicity repeated exposure : Category 2 Pictograms or Hazard symbols |  |  |
| Warning: May be corrosive to metals Warning: Harmful if swallowed, in contact with skin, or inhaled. Danger: Causes severe skin burns and eye damage. Causes serious eye damage. Warning. Health hazard. May cause damage to lungs, eyes, and mucous membranes through prolonged or repeated exposure. Precautionary Statements P234 Keep only in original container. P260 Do not breathe fume/gas/mist/vapors. P261 Avoid breathing fumes/mist/vapors. P264 Wash thoroughly after handling. P270 Do not eat, drink, or smoke when using this product. P271 Use only outdoors or in a well-ventilated area. P280 Wear protective gloves, clothing, and eye and face protection. P301 + P312 If swallowed, call a physician if you feel unwell. P301 + P330 + P331 If swallowed, rinse mouth. Do not induce vomiting. P302 + P352 If on skin, wash with plenty of water. Remove contact lenses if present and easy to do so. Continue rinsing. P303 + P361 + P353 If on skin (or hair) take off immediately all contaminated clothing. Rinse skin with water. P304 + P340 If inhaled, remove person to fresh air and keep comfortable for breathing. P305 + P351 + P338 If in eyes, rinse cautiously with water for several minutes. P308 + P311 If exposed or concerned, call a physician. P312 Call a physician if you feel unwell. P314 Get medical advice/attention if you feel unwell. P330 Rinse mouth. P362 + P364 Take off contaminated clothing and wash it before reuse. P363 Wash contaminated clothing before reuse. P390 Absorb spillage to prevent material damage. P405 Store locked up. P406 Store in corrosive resistant container. P501 Dispose of contents/container in accordance with local/regional/national/international regulations. |  |  |

###### SECTION 3.COMPOSITION/INFORMATION ON INGREDIENTS

| Material Nitric Acid CAS# 7697-37-2 Ceric Ammonium Nitrate CAS# 16774-21-3 Water CAS# 7732-18-5 Total | Wt % 5-6 10-20 75-84 100 | Toxicity 2 ppm (TLV) 244 ppm |
| --- | --- | --- |

SECTION 4. FIRST AID MEASURES

#### EFFECTS OF OVEREXPOSURE

FIRST AID:

Eye Contact: Corrosive to naked eye; in case of contact flush eyes well for 15 minutes, lifting the lower and upper eyelids occasionally.   May cause blindness.  Seek medical attention.

Skin Contact: Obtain medical attention: Corrosive to exposed skin. Flush skin well with water for 15

minutes, wash with soap and water. Remove affected clothing, get medical attention.

Inhalation:  If mist or fumes are inhaled, remove to fresh air.  If not breathing give artificial respiration. Seek medical attention. Effects may be delayed.  May cause chemical burns to the respiratory tract.

Ingestion:   May cause severe and permanent damage to the digestive tract.  Causes gastrointestinal burns and performation of the digestive tract.  Get medical attention immediately.

| SECTION 5. FIRE FIGHTING MEASURES |
| --- |
| Flash Point and Method non-flammable | Autoignition Temp. NA | Flammability Limits In Air | LOWER NA | UPPER NA |

Extinguishing media: Water spray or fog, carbon dioxide and dry chemical.  Do not use organic media.

Special fire fighting procedures: Wear chemically retardant gear and NIOSH approved self-contained breathing apparatus. Thermal decomposition produces irritating and toxic fumes. Contact with oxidizing reagents may cause extremely violent combustion.

SECTION 6. ACCIDENTAL RELEASE MEASURES

SPILLS, LEAKS: Ventilate area of leak or spill. Clean up personnel should wear protective clothing and NIOSH approved respirator. Dike and cover the contaminated areas with absorbent, non-combustible material such as earth, sand, or vermiculite.

#### SECTION 7. HANDLING AND STORAGE

Wash thoroughly after handling.  Remove contaminated clothing and wash before re-use.  Do not breathe dust, mist, or vapor.  Do not expose eyes, skin, or clothing.  Keep container closed tightly.  Avoid contact with combustibles.  Do not use with metal tools or items.  Use with adequate ventilation or respiratory protection. Do not store near combustibles or in direct sunlight.  Store in a cool, dry, well-ventilated area away from incompatible substances.  Separate from metals, alkali, and organics.

SECTION 8. EXPOSURE CONTROL/PERSONAL PROTECTION

Respiratory protection: Wear NIOSH/MESA approved full or half face piece (with goggles) respiratory protective equipment to avoid exposure to vapors above 0.1ppm. A respiratory protection program complying with requirements of 29CFR 1910.134 is recommended.

Ventilation:	Where adequate ventilation is not available, use NIOSH approved vapor respirator with dust, fume and mist filters. Local ventilation through fume hoods or laminar flow stations is also preferred. Keep fumes away from strong bases.

Protective gloves: Skin contact should be minimized through use of rubber gloves.

Other protective equipment:	Steel tipped shoes/eye wash station/chemical safety chemical retardant clothing.  Eye protection: Safety goggles / face shield

SECTION 9. PHYSICAL AND CHEMICAL PROPERTIES

Form :								  Liquid

Appearance :                                                                           Orange

Odor :                                                                 Acrid

pH :                                                                                          < 1

Melting point:                                                                          Not available

Boiling point/Boiling range :                                                 100 oC (water)

Flash point :                                                                             Non-flammable.

Ignition point :                                                                         Will not ignite.

Danger of explosion:                                                               Product is not explosive

Decomposition temperature:                                                 > 150 oC

Vapor density (Air = 1) :                                                        Not available

Volatiles, %:                                                                            75-84

Vapor pressure at 15o C, mm Hg:                                         51 mm Hg at 25 oC

Specific gravity :                                                                     1.16 g/cc

Solubility in / Miscibility:                                                       Completely miscible in water

Evap. Rate (Water = 1):                                                          < 1

##### SECTION 10.  STABILITY AND REACTIVITY

| Stability | Stable X Conditions to avoid: Excess heat , light, confined spaces Unstable |
| --- | --- |
| Incompatible with: Metals/metal powders, reducing agents, strong bases, acetic acid, alcohol, acetone, aniline, hydrogen sulfide, carbides, organic solvents, combustibles, chromic acid, flammables, cyanides, sulfides. Hazardous decomposition products: Nitrogen oxides |
| Hazardous polymerization: | May occur Conditions to avoid: Excess heat, damp. Will not occur X |

SECTION 11. TOXICOLOGICAL INFORMATION ACUTE: LC50 (Inhalation, rat): 1.35 mg/L/4 h (nitrogen dioxide) (anhydrous substance) LDLo (oral, human): 4500 mg/kg (anhydrous substance) (IUCLID) Specific symptoms in animal studies: burns to eyes (rabbit), burns to skin (rabbit) SUBACUTE TO CHRONIC TOXICITY: Bacterial mutagenicity: Ames test: negative OTHER DATA: Corrosive. Vapor inhalation burns mucous membranes; causes coughing, dyspnoea. Inhalation may lead to oedemas in the respiratory tract. Burns skin, eyes (risk of blindness). Swallowing results in damage to mouth esophagus, and gastrointestinal tract; risk of perforation; bloody vomiting; death. SECTION 12. ECOLOGICAL INFORMATION Bioaccumulation : There is no evidence of bioaccumulation. Ecotoxicity : Biologic effects: Toxic effect on fish and plankton. Harmful effect due to pH shift. Forms corrosive mixtures with water even when diluted. Does not cause biological oxygen deficit. Hazardous to drinking water supplies. Fish toxicity: Gambusia affinis LC50: 756 mg/L/96 h Hazard for drinking water: Fish: LC50 > 1500 mg/L. SECTION 13. DISPOSAL CONSIDERATIONS DISPOSAL: Dispose of in accordance with all federal state and local regulations. Send waste to an approved waste disposal facility. SECTION 14. TRANSPORTATION INFORMATION Class 8 PG II UN3264 Shipping Name: Corrosive Liquid, Acidic, Inorganic, N.O.S. (Ceric Ammonium Nitrate and Nitric Acid) SECTION 15. REGULATORY Symbol: C, Corrosive R-Phrase: R: Contact with combustible material may cause fire. R21/22: Harmful in contact with skin and if swallowed. R35: Causes severe burns. R41: Risk of serious damage to eyes. S-Phrases: S17: Keep away from combustible material. S23-36/37/39-45 Do not breathe vapor. In case of contact with eyes, rinse immediately with plenty of water and seek medical advice. Wear suitable protective clothing, gloves, and eye/face protection. In case of accident or if you feel unwell, seek medical advice immediately (show the label where possible). The following component of this product is regulated as toxic a chemical under section 313 or Title III SARA, and 40CFR 372: Nitric Acid CAS# 7697-37-2 SECTION 16. OTHER INFORMATION NFPA Codes: Health: 4 Flammability: 0 Reactivity: 1 R8: Contact with combustible material may cause fire. R35: Causes severe burns. All ingredients of this product are listed on the US TSCA inventory under their parent anhydrous compounds.